## Slide 1
01 - DIFFERENTIAL
01 – ASSEMBLY TIPS
THE BALLS SHOULD “POP” TO
BE INSERTED OR REMOVED
MAKE SURE IT’S FULL TIGHTEN
DIFF GREASE
1
2
3
4
12
5
6
7
6
9
11
8
1
13
10

## Slide 2
BAG – 1 CONTENT
PARTS
PARTS
1 | X-SSS-2.5-2 | M2.5x2mm
BOLTS
01 – SETUP TIPS
TIGHTEN – MORE STEERING
LOOSEN – LESS STEERING
1 | XB1-048-1 | Diff Whell Hub 1
2 | XB1-097 | Diff Aluminum 7075 Shaft
3 | XB1-048-3 | Diff Adjustor Hub
4 | XB1-048-4 | Oring 3x7x2
5 | XB1-048-5 | Diff Hub Pressure Plate
6 | XB1-048-6 | Diff Pressure Plate
7 | XB1-048-7 | Diff 64P 53T Spur Gear
8 | XB1-048-8 | Ceramic Balls
9 | XB1-048-9 | Bearing 4x7x2
10 | XB1-099 | Diff Whell Hub 2
11 | XB1-048-13 | Lock Nut M2
12 | XB1-048-14 | 1.5mmm Shaft
13 | X-WSH-3-5-0.5 | Washer 3x5x0.5